## Slide 1
Techno-economic assessment of a decentralized system for pure hydrogen production via green ammonia decomposition
Dr. Valentina Cechetto
Prof. Dr. Eng. Fausto Gallucci
H2
NH3

## Slide 2: The emission challenge and energy transition
Global greenhouse gas emissions by sector
Source: Climate Watch, the World Resources Institute (2020)
Licensed under CC-BY by the author Hannah Ritchie (2020)
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 0.732 | 0.052 | 0.032 | 0.184
Heat generation
Electricity generation
Transport
Agriculture, Forestry & Land use
18.4%
Waste
Industry
3.2%
5.2%
The energy sector mainly relies on the exploitation of fossil fuels
The world population is consistently growing alongside the worldwide energy demand
Development of strategies to promote the decarbonization of the energy system
Notes: The main idea behind this work is to contribute to development of solutions capable of promoting the decarbonization of the current energy system. The current energy system in fact mainly relies on the use of fossil fuels with tremendous consequences for our planet and for life on it. Literature indeed reports that the solely energy sector comprising electricity generation, heat generation and transport, is responsible for about 73.2 % of the total emissions. Therefore, in a scenario in which the world population is consistently growing alongside the worldwide energy demand, a transition towards a more sustainable energy scenario becomes essential.

## Slide 3: Why ammonia?
Energy storage in the form of dispatchable energy carriers
H2 storage in
liquid carrier compounds
Easy transport over long distances
Easy storage for long time
Possible in-situ decomposition to produce H2 when required
NH3
Existing infrastructure for transport
Existing infrastructure for storage
Carbon free
Suitable for carbon sensitive applications
PEM fuel cell
RENEWABLE ENERGY
Intermittency
H2
Ideal energy carrier
Carbon free
Low volumetric energy density
Low boiling point
Challenging storage and handling
Notes: The exploitation of renewable energy sources plays a fundamental role in the energy transition. However, their intermittent nature represents a challenge for coupling the demand with production and poses grid stability challenges. Energy storage can be regarded as the key to overcome this issue and in particular hydrogen has been gaining attention as the ideal energy carrier. Hydrogen could in fact be produced from water electrolysis exploiting renewable energy and used for power generation when required with zero carbon footprint. However, the low volumetric energy density and the low oiling point of hydrogen make its storage and handling challenging.

## Slide 4: Ammonia decomposition
Chart: Temperature [°C]
| 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800
1 bar | 0.74376 | 0.89776 | 0.95904 | 0.98211 | 0.99139 | 0.99548 | 0.99744 | 0.99845 | 0.99901 | 0.99934 | 0.99954 | 0.99967 | 0.99976
5 bar | 0.44339 | 0.67266 | 0.8341 | 0.91898 | 0.95901 | 0.97796 | 0.98737 | 0.99233 | 0.9951 | 0.99673 | 0.99773 | 0.99837 | 0.99879
10 bar | 0.32714 | 0.53877 | 0.7295 | 0.85462 | 0.92256 | 0.95726 | 0.97519 | 0.98483 | 0.99027 | 0.99348 | 0.99547 | 0.99674 | 0.99759
20 bar | 0.23226 | 0.40745 | 0.59948 | 0.7573 | 0.86025 | 0.91938 | 0.95205 | 0.97029 | 0.98079 | 0.98708 | 0.99099 | 0.99351 | 0.9952
Chart: Temperature [°C]
| 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800
1 bar | 0.74376 | 0.89776 | 0.95904 | 0.98211 | 0.99139 | 0.99548 | 0.99744 | 0.99845 | 0.99901 | 0.99934 | 0.99954 | 0.99967 | 0.99976
5 bar | 0.44339 | 0.67266 | 0.8341 | 0.91898 | 0.95901 | 0.97796 | 0.98737 | 0.99233 | 0.9951 | 0.99673 | 0.99773 | 0.99837 | 0.99879
10 bar | 0.32714 | 0.53877 | 0.7295 | 0.85462 | 0.92256 | 0.95726 | 0.97519 | 0.98483 | 0.99027 | 0.99348 | 0.99547 | 0.99674 | 0.99759
20 bar | 0.23226 | 0.40745 | 0.59948 | 0.7573 | 0.86025 | 0.91938 | 0.95205 | 0.97029 | 0.98079 | 0.98708 | 0.99099 | 0.99351 | 0.9952
NH3
0.5 N2 + 1.5 H2
Conventional system
H2/N2 separation unit
NH3
H2 + N2
H2
Off-gases
Reaction unit
working at high temperature and low pressure
NH3
Permeate: H2
Retentate: N2
Novel technology
MEMBRANE REACTOR
NH3 decomposition reaction into H2 and N2 and high-purity H2 separation are simultaneously performed

## Slide 5: Proof of concept
Chart: Temperature [°C]
| 400 | 425 | 450
Thermodynamic Equilibrium | 96.68 | 97.59 | 98.22
No Membrane | 65.44 | 86.22 | 96.78
Membrane (Permeate at 1 bar) | 72.15 | 98.02 | 99.5
Membrane (Permeate at vacuum) | 99.3 | 99.6 | 99.8
Chart: Temperature [°C]
| 400 | 425 | 450
Membrane (Permeate at 1 bar) | 51.6 | 79.75 | 85.4
Membrane (Permeate at vacuum) | 93.51 | 96.7 | 96.5
NH3
Permeate: H2
Retentate: N2
Experimental conditions | 
ΔP [bar] | 3
Permeate pressure [bar] | 0.01-1
Feed flow rate [LN/min] | 0.5
Membrane | Double-skinned Pd-Ag
Thickness selective layer [μm] | 4.61
Experimental conditions | 
ΔP [bar] | 3
Permeate pressure [bar] | 0.01-1
Feed flow rate [LN/min] | 0.5
Membrane | Double-skinned Pd-Ag
Thickness selective layer [μm] | 
Compared to conventional systems, in a membrane reactor:
Comparable or higher NH3 conversion can be achieved at lower temperature (higher efficiencies)
High-purity H2 is recovered
Cechetto, V.; Di Felice, L.; Medrano, J.A.; Makhloufi, C.; Zuniga, J.; Gallucci, F. H2 production via ammonia decomposition in a catalytic membrane reactor, Fuel Processing Technology, 2021, Volume 216, 106772, https://doi.org/10.1016/j.fuproc.2021.106772.
Notes: A literature study revealed Pd-based membranes as the most promising ones for high purity hydrogen recovery. Thus, a first proof of concept of the technology was carried out with the aim to assess the advantages implied by the choice of a Pd-based membrane reactor over a conventional system.
The result of this study demonstrated that compared to a conventional system, higher or comparable NH3 conversion can be achieved in a MR at lower temperature, which results in higher efficiencies. Moreover, it was proven that high purity hydrogen could be simultaneously recovered.
Improved performance could then be achieved by increasing the driving force across the membrane: through the application of vacuum at the permeate side of the membrane in fact higher recoveries as well as NH3 conversions could be achieved. Interestingly, in this case, NH3 conversion higher than the thermodynamic equilibrium one without the membrane could be achieved.

## Slide 6: Proof of concept
NH3
Permeate: H2
Retentate: N2
Experimental conditions | 
ΔP [bar] | 3
Permeate pressure [bar] | 0.01-1
Feed flow rate [LN/min] | 0.5
Membrane | Double-skinned Pd-Ag
Thickness selective layer [μm] | 4.61
Experimental conditions | 
ΔP [bar] | 3
Permeate pressure [bar] | 0.01-1
Feed flow rate [LN/min] | 0.5
Membrane | Double-skinned Pd-Ag
Thickness selective layer [μm] | 
Chart: Reaction pressure [Bar]
| 2 | 3 | 4 | 5 | 6
Ammonia Conversion (%) | 0.988 | 0.99479 | 0.99617 | 0.99688 | 0.99676
H2 recovery (%) | 0.49793 | 0.78577 | 0.86607 | 0.90451 | 0.92361
H2 purity (%) | 0.99993 | 0.99989 | 0.99985 | 0.9998 | 0.9998
Compared to conventional systems, in a membrane reactor:
Higher NH3 conversion can be achieved at similar pressures (higher compactness)
Lower purities of H2 recovered
Cechetto, V.; Di Felice, L.; Medrano, J.A.; Makhloufi, C.; Zuniga, J.; Gallucci, F. H2 production via ammonia decomposition in a catalytic membrane reactor, Fuel Processing Technology, 2021, Volume 216, 106772, https://doi.org/10.1016/j.fuproc.2021.106772.
Notes: It was also demonstrated that compared to conventional systems, higher ammonia conversion can be achieved in a membrane reactor at similar pressures, which results in higher compactness. Although a pressure increase results in lower purities of hydrogen recovered, the removal of hydrogen from the reaction zone indeed enhances the reaction rates and shifts the reaction thermodynamics which in turn enhance ammonia conversion counterbalancing the ammonia conversion decrease that is on the other hand expected according to the le chateliers principle

## Slide 7: The challenge of H2 purity
PEMFC specifications requires residual NH3 concentration in the H2 feed < 0.1 ppm.
Economic viability
Implementation of a cleanup unit downstream of the MR
With no sorbent
With sorbent
Chart: Time [min]
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150 | 155 | 160 | 165 | 170 | 175 | 180
NH3 concentration int the permeate [ppm] | 68.094 | 69.018 | 69.64 | 70.045 | 71.079 | 70.4 | 72.158 | 73.755 | 71.21 | 71.611 | 71.798 | 70.487 | 73.133 | 73.851 | 74.176 | 72.448 | 71.883 | 72.222 | 5.097 | 2.519 | 1.596 | 0.935 | 1.048 | 0.683 | 0.471 | 0.461 | 0.326 | 0.318 | 0.563 | 0.094 | 0.392 | 0.165 | 0.326 | 0.613 | 0.444 | 0.07
The reactor can be operated at lower temperatures with higher residual NH3 concentration
Higher energy efficiency
Less selective membranes can be implemented
T= 450°C, P=3 bar, NH3 feed flow rate =0.5 LN/min
Thickness selective layer 1μm
Sorbent: zeolite 13X
Cechetto, V.; Gutierrez Martinez, R.; Di Felice, L.; Gallucci, F.; Ultra-pure hydrogen production via ammonia decomposition in packed bed membrane reactors, International Journal of Hydrogen Energy, 2022, Volume 47, https://doi.org/10.1016/j.ijhydene.2022.04.240.
Notes: When targeting the production of hydrogen to be used as fuel for PEMFC, NH3 concentration should not exceed 0.1 ppm. However, the results of the proof of concept proved the achievement of this target challenging. In fact such a low concentration was not achieved in any of the investigated operating conditions. A possible solution to overcome thi challenge is the implementation of a hydrogen cleanup unit downstream of the MR. Both the strategies proved technically feasible. However, strategy 2 proved more economically viable.
Next to the technical feasibility in fact, the use of thinner membranes which already implies lower costs due to the fact that a lower amount of palladium is used for each membrane fabrication, also allows for higher permeation flux through the membrane. This translates into the fact that costs are further lowered as a lower amount of membranes is needed.
Moreover, the fact that the achievement of the purity target is guaranteed by the presence of the cleaning unit allows the reactor to be operated at lower temperatures, which improves the energy efficiency of the system and also implies that less selective membranes can be implemented. This in turn translates in the possibility to use also membrane less performing and cheaper than Pd-based ones.

## Slide 8: Research question
Target:
500 kg/day of H2
H2 purity = 99.97%
Max NH3 concentration in H2 stream = 0.1 ppm
14
NH3
Permeate: H2
Retentate: N2
Is the membrane reactor-based system economically competitive compared to a conventional system?
Studies available in literature calculated the costs of hydrogen production, but a comparative study addressing a techno-economic assessment at different plant capacities and system configurations is not available.
This work:
Techno-economic assessment of a decentralized plant for hydrogen production from ammonia decomposition
H2 for direct use in PEM fuel cells
Applications: stationary applications (a), on-board vehicle applications (b), and refuelling stations (c)
€
?
?
?
NH3
H2
?
?
?
Conventional or MR-based system?
Notes: Decentralized plant in which hydrogen is produced in a relatively small-scale production system to supply local demand

## Slide 9
Design of conventional system for green NH3-derived hydrogen production
H2 production: 500 kg/day
Final H2 application:1) Stationary applications (SA) 2) On-board vehicle applications (O-VA) 3) refueling stations for vehicle applications (R-VA)
Evaluation of operating conditions allowing for minimization of cost of hydrogen (COH)
Evaluated reactor operating conditions: T=450-550°C and P=1-20 bar
Design of the MR-based system
Reactor operating conditions: TMR=TCR-50°C and PMR=PCR
Optimization of the MR-based system design
Investigation of process parameters that optimize COH
Methods

## Slide 10
Plant Component | Cost [k€]
Component W | A
Component X | B
Component Y | C
Component Z | D
Bare Erected Cost [BEC] | A+B+C+D
Direct costs as percentage of BEC | 
Total Installation Costs [TIC] | 80% BEC
Total Direct Plant Cost [TDPC] | BEC+TIC
Indirect Costs [IC] | 14% TDPC
Engineering procurement and construction [EPC] | TDPC+IC
Contingencies and owner’s costs | 
Contingency | 10% EPC
Owner’s cost | 5% EPC
Total contingencies & OC [C&OC] | 15% EPC
Total Overnight Cost [TOC] | EPC+C&OC
Cost O&M fixed | 
Maintenance | 2.5% TOC
Insurance | 2% TOC
Labor | 27991 €/year/pp1
1 https://www.payscale.com/research/NL/Job=Chemical_Process_Operator/Salary
2 https://www.iea.org/reports/global-hydrogen-review-2021/executive-summary
3 S. Richard, A. Ramirez Santos, and F. Gallucci, “PEM genset using membrane reactors technologies An economic comparison among different e-fuels”, International Journal of Hydrogen Energy
4 https://www.msesupplies.com/products/1kg-molecular-sieves-13x-pellets-spheres?variant=31758805205050
COST O&M variable | 
Green NH3 | 853.92 €/ton 2
Electricity | 0.085 €/kWh 3
Catalyst | 143 €/kg 3
Zeolite 13X | 43.7 €/kg 4
Membrane | 6000 €/m 3
Assumptions | 
Plant availability | 90%
Plant lifetime (n) | 25 years 3
Catalyst lifetime | 5 years 3
Lifetime Zeolite 13X | 5 years
Membrane lifetime | 5 years
Discount factor (i) | 8% 3
Methods: economic assessment

## Slide 11
H2 production from NH3: the conventional and the MR-based systems
Conventional system
Stationary applications
Vehicle applications
Membrane reactor-based system
Stationary applications
Vehicle applications
13
Design choices:
Catalyst: Ru/Al2O3
NH3 removal unit: TSA (2 beds configuration)
N2 removal unit: PSA (4 beds configuration)

## Slide 12
Design of the conventional process for SA

## Slide 13
Design of the conventional process for VA

## Slide 14
Optimization of the conventional system
Chart: Pressure [bar]
| 1 | 5 | 10 | 15 | 1 | 5 | 10 | 15 | 1 | 5 | 10 | 15
Share CAPEX | 0.38045 | 0.37793 | 0.41727 | 0.41562 | 0.37696 | 0.37536 | 0.4059 | 0.41637 | 0.38243 | 0.38007 | 0.40562 | 0.41083
Share OPEX fixed | 0.35317 | 0.35196 | 0.37086 | 0.37006 | 0.3515 | 0.35073 | 0.3654 | 0.37043 | 0.35412 | 0.35299 | 0.36531 | 0.36777
Share OPEX variable | 6.4 | 6.2874 | 6.2804 | 6.3418 | 6.5142 | 6.4051 | 6.4009 | 6.3955 | 6.6449 | 6.5377 | 6.5376 | 6.5335
Chart: Pressure [bar]
Share CAPEX | 0 | 0.4005 | 0.39796 | 0.42109 | 0.41692 | 0.41896 | 0.40189 | 0.40004 | 0.42313 | 0.42387 | 0.42363 | 0.40444 | 0.40283 | 0.42542 | 0.42594 | 0.42658 | 0
Share OPEX fixed | 0 | 0.53322 | 0.532 | 0.54311 | 0.54111 | 0.54209 | 0.53389 | 0.533 | 0.54409 | 0.54445 | 0.54433 | 0.53511 | 0.53434 | 0.54519 | 0.54544 | 0.54575
Share OPEX variable | 0 | 6.6156 | 6.469 | 6.5829 | 6.5691 | 6.6251 | 6.7516 | 6.6057 | 6.7321 | 6.7241 | 6.7163 | 6.9206 | 6.7722 | 6.8947 | 6.8899 | 6.8905
Chart: Pressure [bar]
Share CAPEX | 0 | 0.51431 | 0.51247 | 0.53543 | 0.53113 | 0.53264 | 0.51566 | 0.51451 | 0.53744 | 0.53802 | 0.53724 | 0.51818 | 0.51728 | 0.53969 | 0.54004 | 0.54014
Share OPEX fixed | 0 | 0.58789 | 0.58701 | 0.59803 | 0.59597 | 0.5967 | 0.58854 | 0.58799 | 0.599 | 0.59928 | 0.59891 | 0.58975 | 0.58932 | 0.60008 | 0.60025 | 0.6003
Share OPEX variable | 0 | 6.8767 | 6.7194 | 6.7757 | 6.7277 | 6.7624 | 7.0142 | 6.8581 | 6.9249 | 6.8808 | 6.8506 | 7.1854 | 7.0265 | 7.0877 | 7.0453 | 7.0223 | 0
Stationary applications
(SA)
On-board vehicle applications
(O-VA)
Refueling stations for vehicle applications (R-VA)
COH in the conventional system is minimized with the reactor operated at T=450 °C and 5 bar
The process is OPEX-intensive with the cost of the NH3 feedstock being the main contributor to COH

## Slide 15
Design of the MR-assisted process for SA/VA
The outstanding performance of Pd-based membranes allows to remove the PSA unit

## Slide 16
Optimization of MR-based system
TMR=TCR-50°C = 400 °C
PMR=PCR = 5 bar
H2
NH3
Chart: H2 recovery
| 0 | 0 | 0 | 0 | 0 | 0.76720436620880628 | 0.77679442078641725 | 0.78638447536402689 | 0.79597452994163609 | 0.80556458451932489 | 0.81515463909685204 | 0.82474469367446657 | 0.8343347482520771 | 0.84392480282968652 | 0.85351661536844425 | 0.86310676210564319
NH3 feedstock | 8.9803 | 8.8695 | 8.7613 | 8.6557 | 8.5812 | 8.5865 | 8.5918 | 8.5971 | 8.6024 | 8.6077 | 8.613
Fraction of H2 to burner | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0033174 | 0.015652 | 0.027698 | 0.039466 | 0.050966 | 0.062209 | 0.073201
Minimum NH3 feedstock requirement
Objective
Minimization of the NH3 feedstock
Reactor optimization Process optimization
A higher recovery reduces the available heat from the combustion of the retentate, which leads to an increased quantity of fuel that must be burned to sustain the NH3 decomposition reaction and that, in turn, implies a greater flow rate of NH3 to be processed.
The cost of NH3 feedstock is the main contributor to COH
Notes: From a reactor-centric perspective, the greater the hydrogen recovery achieved, the higher is the separation efficiency of hydrogen from ammonia, which results in a lower ammonia flow rate required at the process inlet. However, when considering the whole NH3-to-H2 process, the decision to operate the reactor while maximizing hydrogen recovery proves non economically convenient. This is because a higher recovery reduces the available heat from the combustion of the retentate, which leads to an increased quantity of hydrogen that must be burned to sustain the ammonia decomposition reaction and that, in turn, implies a greater flow rate of ammonia to be processed in the reactor.

## Slide 17
Process | Conventional |  |  | MR-assisted | 
Application | Stationary | Vehicle on-board | Vehicle refueling stations | Stationary and vehicle on-board | Vehicle refueling stations
Feedstock |  |  |  |  | 
NH3 [kg/h] | 151.03 | 153.46 | 153.46 | 146.15 | 146.15
Thermal input [kWLHV] | 780.50 | 793.09 | 793.09 | 755.27 | 755.27
Chemical products |  |  |  |  | 
H2 [kg/h] | 20.83 | 20.83 | 20.83 | 20.83 | 20.83
Thermal output [kWLHV] | 693.92 | 693.92 | 693.92 | 693.92 | 693.92
Cold Gas Efficiency (CGE) | 88.91% | 87.50% | 87.50% | 91.88% | 91.88%
Electricity |  |  |  |  | 
Air blower [kWel] | 1.95 | 2.29 | 2.29 | 1.87 | 1.87
Hydrogen booster [kWel] | - | - | 28.33 | 19.33 | 37.09
Hydrogen compressor [kWel] | - | - | 46.04 | - | 45.85
Vacuum pump [kWel] | - | - | - | 29.69 | 29.69
Total electricity [kWel] | 1.95 | 2.29 | 76.74 | 50.89 | 114.50
Overall plant efficiency (ηtot) | 88.69% | 87.24% | 79.78% | 86.08% | 79.78%
Technical assessment

## Slide 18
Technical assessment
 | Conventional process Stationary applications | Conventional process Vehicle applications | MR-assisted process Stationary and vehicle applications
Reactor operating conditions |  |  | 
Reaction temperature [°C] | 450 | 450 | 400
Reaction pressure [bar] | 5 | 5 | 5
Permeate pressure [bar] | - | - | 0.1
Feedstock |  |  | 
NH3 flow rate at reactor inlet | 151.03 kg/h 8.87 kmol/h | 153.46 kg/h 9.01 kmol/h | 146.15 kg/h 8.58 kmol/h
Energy requirement |  |  | 
Thermal input [kW] | 127.51 | 129.58 | 123.72
KPI |  |  | 
NH3 conversion | 97.8% | 97.8% | 99.1%
H2 recovery | - | - | 80.6%
Reactor efficiency (ηreactor) | 96.2% | 96.2% | 79.2%* (97.4%**)
 | 5.8 kg/kg | 5.8 kg/kg | 7.0 kg/kg* (5.7 kg/kg**)
* Calculated considering as valuable reaction product only hydrogen available at the reactor’s permeate side ** Calculated considering as valuable reaction product both the hydrogen available at the reactor’s permeate and retentate sides |  |  | 
 | Conventional process Stationary applications | Conventional process Vehicle applications | MR-assisted process Stationary and vehicle applications
Reactor operating conditions |  |  | 
Reaction temperature [°C] | 450 | 450 | 400
Reaction pressure [bar] | 5 | 5 | 5
Permeate pressure [bar] | - | - | 0.1
Feedstock |  |  | 
NH3 flow rate at reactor inlet | 151.03 kg/h 8.87 kmol/h | 153.46 kg/h 9.01 kmol/h | 146.15 kg/h 8.58 kmol/h
Energy requirement |  |  | 
Thermal input [kW] | 127.51 | 129.58 | 123.72
KPI |  |  | 
NH3 conversion | 97.8% | 97.8% | 99.1%
H2 recovery | - | - | 80.6%
Reactor efficiency (ηreactor) | 96.2% | 96.2% | 79.2%* (97.4%**)
 | 5.8 kg/kg | 5.8 kg/kg | 7.0 kg/kg* (5.7 kg/kg**)
* Calculated considering as valuable reaction product only hydrogen available at the reactor’s permeate side ** Calculated considering as valuable reaction product both the hydrogen available at the reactor’s permeate and retentate sides |  |  | 

## Slide 19
Is the packed bed MR technology competitive compared to the packed bed conventional technology?
Scenario 1: stationary applications
Both in the conventional and in the MR-based systems the COH is 6.95 €/kg
No economic advantage from utilization of the packed bed MR technology
Scenario 2.2: refueling stations for vehicle applications
Similar conclusions to scenario 2.1 with COHconventional=7.57 €/kg and COHMR-assisted=7.38 €/kg
Conventional system
COH = 7.15 €/kg
COH = 6.95 €/kg
Chart: 
| CAPEX | OPEX fixed | OPEX variable
Sales | 0.0554 | 0.0512 | 0.8934
CAPEX
OPEX fixed
OPEX variable
Chart: 
| CAPEX | OPEX fixed | OPEX variable
Sales | 0.0565 | 0.0516 | 0.8919
OPEX variable
CAPEX
OPEX fixed
Scenario 2.1: on-board vehicle applications
96.64%
NH3 feedstock
98.36%
NH3 feedstock
MR-assisted system
Economic assessment
Notes: As a final step, a techno-economic assessment of the MR technology was performed focusing on systems for the decentralized production of H2 from NH3.
3 different scenarios were investigated: the production of hydrogen for stationary applications, the production of hydrogen for on-board vehicle applications and the production of hydrogen for refuelling stations.
The results of the techno-economic assessment demonstrated that in case of hydrogen production for stationary applications, no advantage is given by the utilization of the packed-bed MR technology.
Conversely, the technology was proved to be more economically competitive when targeting the production of hydrogen for vehicle applications.
More in detail, the study revealed the production of hydrogen from ammonia to be an OPEX intensive process, with the cost of NH3 feedstock being the main contributor to the final COH.
Thus, the lower COH in the MR-assisted system can be mainly ascribed to the fact that in this configuration a lower ammonia feedstock is required.

## Slide 20
Chart: Percentage change from initial value [%]
Economic assessment
Sensitivity analysis and forecasting
Chart: Cost of Green NH3 [$/ton]
| 2020 | 2030 | 2050
 | 928.17 | 409.86 | 301.41
Year | Cost of NH3 [€/ton] | COH [€/kg]
2020 | 853.92 | 6.95
2030 | 377.07 | 3.60
2050 | 277.30 | 2.90
Chart: Cost of green NH3 [€/ton]
| 853.91639999999995 | 843.91639999999995 | 833.91639999999995 | 823.91639999999995 | 813.91639999999995 | 803.91639999999995 | 793.91639999999995 | 783.91639999999995 | 773.91639999999995 | 763.91639999999995 | 753.91639999999995 | 743.91639999999995 | 733.91639999999995 | 723.91639999999995 | 713.91639999999995 | 703.91639999999995 | 693.91639999999995 | 683.91639999999995 | 673.91639999999995 | 663.91639999999995 | 653.91639999999995 | 643.91639999999995 | 633.91639999999995 | 623.91639999999995 | 613.91639999999995 | 603.91639999999995 | 593.91639999999995 | 583.91639999999995 | 573.91639999999995 | 563.91639999999995 | 553.91639999999995 | 543.91639999999995 | 533.91639999999995 | 523.91639999999995 | 513.91639999999995 | 503.91639999999995 | 493.91639999999995 | 483.91639999999995 | 473.91639999999995 | 463.91639999999995 | 453.91639999999995 | 443.91639999999995 | 433.91639999999995 | 423.91639999999995 | 413.91639999999995 | 403.91639999999995 | 393.91639999999995 | 383.91639999999995 | 373.91639999999995 | 363.91639999999995 | 353.91639999999995 | 343.91639999999995 | 333.91639999999995 | 323.91639999999995 | 313.91639999999995 | 303.91639999999995 | 293.91639999999995 | 283.91639999999995
 | 6.9498 | 6.8796 | 6.8095 | 6.7393 | 6.6692 | 6.599 | 6.5289 | 6.4587 | 6.3886 | 6.3184 | 6.2483 | 6.1781 | 6.108 | 6.0378 | 5.9677 | 5.8975 | 5.8273 | 5.7572 | 5.687 | 5.6169 | 5.5467 | 5.4766 | 5.4064 | 5.3363 | 5.2661 | 5.196 | 5.1258 | 5.0557 | 4.9855 | 4.9154 | 4.8452 | 4.7751 | 4.7049 | 4.6348 | 4.5646 | 4.4945 | 4.4243 | 4.3542 | 4.284 | 4.2138 | 4.1437 | 4.0735 | 4.0034 | 3.9332 | 3.8631 | 3.7929 | 3.7228 | 3.6526 | 3.5825 | 3.5123 | 3.4422 | 3.372 | 3.3019 | 3.2317 | 3.1616 | 3.0914 | 3.0213 | 2.9511
2020 | 6.9497
2030 | 3.6045
2050 | 2.9046
https://www.iea.org/reports/global-hydrogen-review-2021/executive-summary

## Slide 21
Conclusions
The MR technology holds significant potential in advancing the decarbonization of the current energy system.
NH3
Permeate: H2
Retentate: N2
In a membrane reactor for H2 production from NH3:
Higher efficiency and compactness compared to a conventional system are achieved
Optimization is possible by tuning the membrane separation performance, the membrane area and the operating conditions
Fuel cell-grade H2 production is possible with the addition of a relatively inexpensive sorption unit downstream of the reactor.
From an economic point of view, the recovery of H2 from green NH3 using MRs can be achieved at lower costs compared to the benchmark technology.
Notes: In this last slide I would therefore like to summarize the main outcomes of my work.
All in all, this findings can lead to the conclusion that the MR technology holds potential in advancing the decarbonization of the current energy system.

## Slide 22
Thank you for your attention